Techrider  „POW – 2045“

Stage:

Dimensions:  minimum 10 m width x 12 m depth x 5 m height.

Floor: white|grey dancefloor (or black/grey wooden splinterproof floor).

Black Sidecurtains

Backdrop white preferred

Stage setting: 1 fake laptop that is going to be broken during the performance               	                     	                     (+ fake power and sound connection ).    	     	                	                                                                           	                     7 x bandages from rig to floor, taped with PVC tape.

Laptop and bandages are provided by the company.

Sound:

Audience: minimum 2 x high mid range speakers, hanging from rig.                                         	     minimum 2 x subwoofers under the audience.

Stage: 2 x high mid range speaker + 2 subwoofers.

Mixer: 2 x stereo inputs asignable to 2 x stereo and 1 mono outputs                                      (1 stereo for speakers on stage, 1 stereo for speakers for audience, 1 mono for subwoofer under audience).

Soundsource (laptop) at FOH.

Light:

13 x ETC Source 25º-50º 750W

7 x PAR 62 CP62 1000W

4 x FRESNEL 1000W

Video

Projector: minimum 10.000 Lumen, minimum resolution: HDTV 1.080p (1.920 x 1.080)
aspect ratio: 16:9, minimum contrast ratio: 7.500 :1, Lens: 0.8- 2.8 : 1 (exact ratio depends on location)

Position: hanging at minimum 5 m from stage level.                                                      Projection has to cover the backwall, around 1,5m of the side walls and minimum 9m of depth on the floor (see plot)

HD Quality connection from laptop at FOH to projector (HDMI).

IMPORTANT: THE PLOT IS ONLY A MODEL TO VISUALICE THE SET UP, IT IS NOT THE FINAL PLOT. PLEASE, SEND US THE PLOT OF YOUR LOCATION AND WE WILL PROVIDE YOU THE EXACT POSITIONS ACCORDING TO YOUR SPACE.

Team members:

Raphael Hillebrand (Choreograph & dancer) mail@raphael-hillebrand.com

Christian Mio Loclair (Dance media artist & dancer) info@princemio.net

Nikola Pieper (Technical direction) nikola.rawfile@gmail.com.net